## Slide 1: LUMINA
ADVANCED TECHNOLOGY
OPTICAL FLUID

## Slide 2: IMAGING FROM FILM
The Naked Eye: Personal View
Reproductive Imaging
  Wet Darkroom
  Digital Scan
All Three Imaging methods:
Are subject to and limited by optic’s laws
Are subject to the imaging method’s capabilities and limitation

## Slide 3: REPRODUCTIVE IMAGING
Wet Darkroom
  Transfers data from one medium to another
  Laborious process
  Low reproducibility even by same operator
  Output media dependent
  Good to poor fidelity to the original
  Second generation duplicates unlike original

## Slide 4: Reproductive Imaging Methods Compared
Wet Darkroom
Digital Scan
Transfers data from one decaying medium to another decaying medium
Laborious process
Difficult and laborious repetitive iteration or editing
Original always needed
Low fidelity of Second generation duplicates
Preserves data from one decaying medium to non-decaying numbers.
Relatively Simple process
Easy repetitive iteration or editing.
Original needed the first time only.
Identical second generation duplicates

## Slide 5: Optical Limitations of DRY Imaging from Film
Light going through dry film is subject to some Scattering at the film grain. Consequences:
    Lower contrast
    Emphasized grain
    Reduction in color saturation
    Over emphasis on scratches and dust
    Reduced dynamic range
  Limitations shared by analog and digital methods but can be overcome for both.

## Slide 6: DRY Imaging from Film PHYSICAL limitations
Film Curvature
  Correction requires glass: negative consequences:
  Additional refraction, -Loss of sharpness and contrast
  Use of Anti Newton Glass: Loss of sharpness and contrast.

## Slide 7: Optical Advantages of FLUID Imaging from Film
Elimination of air / film interphase
  Elimination of Light scattering at grain =
    Higher contrast
    Greater sharpness
    Higher fidelity rendition of grain
    Higher color saturation
    Dust and scratch-reduction or elimination
    Rich gradation

## Slide 8: PHYSICAL Advantages of FLUID Imaging from Film
Film Flatness = Uniform plane of focus
Glass needed only on one side
Glass can be placed in non-refractive position
  On side of light relative to film’s emulsion
Avoids Anti Newton Glass

## Slide 9: The Ideal Imaging Fluid
Causes no physical damage to Film or equipment
  Not a solvent: Does not dissolve film backing or emulsion or drums, if drum scanned.
Chemically inert under use or storage conditions
  Try the ScanScience Cup Test.
Odourless
Operator Safe:
  Low Vapour toxicity:
    Free of Carcinogens, or target-organ toxics,
    Free of aromatic Hydrocarbons, Olefins and n-Hexane
  Not flammable under normal use conditions
    High Flash Point
Non toxic ?
  No such thing, all hydrocarbons are toxic by ingestion

## Slide 10: Imaging Fluids: Special Concerns with Legacy Film
Many Film variants
  Nitrocellulose > Other cellulose backed films containing aromatic plasticizer: Tri-Phenyl Phosphate (TPP)
  Fluids containing aromatic hydrocarbons can extract the TPP : cause dimensional changes to film, increase brittleness
    Try ScanScience Cup Test: tests solvent aggressiveness of fluid against Polystyrene a polyaromatic polymer.
    Fluids that damage polystyrene can also extract TPP and may damage scanner drums

## Slide 11: IMAGING FLUIDS EVOLUTION
Developers of the Drum Scanner run Into Newton, Rings, they knew those could be eliminated by fluid mounting.
These guys tried baby oil, and it worked.
The first generation imaging fluid was born!

## Slide 12: Results were great...
But the drudgery had begun.
As It turned out, baby's bottoms were better with oil, not drums.
Cleaning the drum required nasty, volatile and smelly stuff.
If it were possible to eliminate the cleaning that would be great!
There had to be a better way. A Better way?

## Slide 13: A better way? Really?
Why not use the smelly volatile stuff used for cleaning the scanning oil as the scanning fluid.....
Voila, it evaporated after use no cleaning needed!
The Second Generation imaging fluid was born!
The cleaner, now the scanning fluid: the smell was the same, bad.
Ah! but a great time saver. That was real progress.
With the second generation scanning fluids Baby Oil went back to being baby oil and
The cleaning drudgery was gone.

## Slide 14: All That Happened In.... THE LAST CENTURY
Not bad for empirical DIY.

## Slide 15: Primary on Newton
Light that strikes two reflective surfaces in close proximity and a slight angle to each other yields two wave fronts which reinforce each other when in phase or destruct when out of phase.
The result is a series of lighter or darker rings.
If the reflective surfaces are kept parallel, the resulting wave fronts are both in phase: therefore, No Newton rings!
But, glass, if used to flatten film is a refractive element that degrades the image. A trade off.

## Slide 16: Avoiding Newton Rings A better way
  Filling the air space between the two reflective surfaces with a fluid:
    Forces the film into a flat plane
    Eliminates the air space between reflective surfaces, makes the surfaces parallel and banishes Newton Rings.
  Without fluid scanning, drum scanners could have not become a commercial reality.
  The same technology is available to all scanners

## Slide 17: Oil-type Imaging Fluids Pros
THE PRO’S
  Scanning Oils are practically Chemically inert to film and scanner drums.
  The Oils high molecular contributes to their low volatility and solvency.
  Oils have no tendency to flash off at the edges of the fluid mount.

## Slide 18: Oil-type Imaging Fluids
PRO’S CONTINUED
  Scanning Oils are stable in storage because they are devoid of the reactive and smelly components natural to less pure petroleum hydrocarbons
  The Oils low volatility means no vapours released
  Oils are essentially not flammable. Big plus!
  The Oils high viscosity and low volatility help maintain a good temporary bond between the components of the fluid mount. No flash off.

## Slide 19: First Generation Scanning Fluids
THE PROS, ...CONTINUED
That was the good news!

## Slide 20: Oil-type Imaging Fluids CONS
Like bad guests, they won't go away when the party is over and need to be forcefully expelled.
Removing the oil requires dry wiping / dilution with other hydrocarbon solvents which are volatile, and potentially flammable.
Cleaning solvents solvent power must be high enough to remove tape residues. The added solvency can be incompatible with the drum or the coatings of some scanner glass beds.

## Slide 21: Scanning fluids The Second Generation
Main advantages: no clean up required.
Self cleaning, evaporate quickly after the scan.
Main disadvantage:
  High volatility = vapour build up,
  Highly flammable below the freezing point.
  Gasoline-like smell,
  Substances present: those normally contained in less refined, cheaper, petroleum distillates.
    Aromatic and olefinic hydrocarbons

## Slide 22: NEW TECHNOLOGY
LUMINA
Third Generation
THE CONVERGENCE OF CHEMISTRY AND PHYSICS

## Slide 23: LUMINA The Ideal Imaging Fluid
  A 'Lens'. -not a solvent: will not damage film or equipment.
  Lumina is an inert optical medium
  Earth and Operator friendly: Good for your image and you.
High purity and consistent quality
  Odorless
  Doesn't' t flash-off while scanning
  Dries clean, leaves no residues
  NOT flammable at Room Temperature
  Low vapour toxicity
  Similar Refractive index as film

## Slide 24: The ScanScience Cup Test
Polystyrene foam is highly susceptible to attack by solvents, particularly those containing aromatic and cyclic hydrocarbons. As a rule, these substances have greater solvency.
The cup at the center is a new cup. The cup at the left contained LUMINA for 24 hours. The cup at the right contained a second generation scanner fluid during 24 hours.
Try the test yourself before trusting your film or scanner to an imaging fluid.

## Slide 25: LUMINA
Breathing life on your Images
See us at www.scanscience.com